This project has been funded with support from the European Commission. This document content reflects the views only of the author, and the Commission cannot be held responsible for any use which may be made of the information contained therein.

airsh | airmon | gpp-air-coremix.pd
& AIR platform phase-one context

SYNOPSIS
    airsh :: AIR shell, a simple air-coremix.pd control shell to demonstrate
    OSC parameters that control the AIR core mixer and AIR console | B-AIR
    project Creative Europe 2020-2023

This manual, a part of airsh documentation, describes broader context of the web audio/control framework concieved to support the B-AIR project's AIR platform.

PUREDATA gpp-air-coremix.pd ELEMENT [server-side]
    OSC-controlled puredata core mixer for AIR platform:

gpp-air-coremix.pd <num.input.channels> <OSC.inaddress> <OSC.outaddress>

    Air core mixer will automatically connect to the <jackd> / <jacktrip>
    -provided channels via puredata input [adc~] and output [dac~]. Although
    technically unlimited, within this setup (AIR platform) the core mixer
    will provide stereo master output and a separate prelisten-bus (as an
    audio-premonitoring option). The number of the input channels is
    arbitrary, set as a creation argument to the core mixer. gpp-air-coremix
    will take the following creation arguments:

    [=] Number of channels (creation arg)
    [=] OSC receiver address and port (creation arg)
    [=] OSC sender (backlink) port (creation arg)
    [-] inlet1 : puredata [netreceive] control input (debugging purposes)
    [-] inlet2 : direct mixer input (debugging purposes)

gpp-air-coremix and jacktrip
    gpp-air-coremixer is primarily intended to be used with Stanford CCRMA
    jacktrip audio networking solution, based on Jack server, primarily in
    hub mode, following two possible audio-scheme scenarios, which differ in
    network-bandwidth demands, quality of user experience and flexibility:

    [ full ] good networking conditions: each client broadcasting their
    channels and receiving all but themselves (jacktrip hubpatch mode 2).
    gpp-air-console, a separate part of gpp-air-coremix, serves the purpose
    of monitoring and controlling this proces [#] and, above all, master
    mixing. In this scenario, each client will mix their own master and
    prelisten bus (via gpp-air-console). In this scenario, bandwidth issues
    may affect the very structure of mix(es).
    .
    [ light ] poor networking conditions: each client broadcasting their own
    channels but receiving only final mix (jacktrip hubpatch mode 0). Master
    mixer will also receive prelisten bus, but this one is mixed by master
    (gpp-air-coremix). A single prelisten-bus is established, available to
    the master-mixer but not for the other remote members. In this scenario,
    bandwidth issues may cause serious delay in perception of the final mix
    feedback.

    Links, explaining the context:

    [OSC protocol] https://ccrma.stanford.edu/groups/osc/index.html

    [jacktrip] https://ccrma.stanford.edu/software/jacktrip/	https://ccrma.stanford.edu/groups/soundwire/software/jacktrip/

    [jack server] https://jackaudio.org/

    .

WHO CAN CONNECT
    [jacktrip] Any client that can run and make use of CCRMA Jack / jacktrip
    can join. According to our pre-testing even connection via modern
    smartphones works decently. Jack / jacktrip is free software solution.
    [all open-source software]
    .
    [gpp-air-console] Any client that can run full installation of puredata
    0.51+ [open-source software]
    .
    [airsh] Any client that can run Perl programming language v5.28 or
    higher "https://www.perl.org/". Air shell is actually a simple OSC
    sender so it can be easily implemented in different software
    environments. All processing is done by gpp-air-coremix.
    .

CONNECTIVITY
    A channel input can be connected either MONO or STEREO. Currently,
    there's no option to recognize whether the jack has been mono or stereo
    connected within PD, so only manual option remains:

    <ch> mono : set selected channels into mono mode
    <ch> stereo : set selected channels into stereo mode
    mono : shortcut to set mono mode globally
    stereo : shortcut to set stereo mode globally

    IMPORTANT A mono wire should be connected to both stereo inputs in order
    to assure proper operation.

    A stereo/mono led indicator on the top of each channel fader shows the
    stereo/mono state.

CONTROL WORKFLOW
  airmix and airmon control and monitoring OSC streams

***client | user action->[airsh or a midi mixer controller connected / via gpp-air-midisender] ===> airmix_protocol ===> [gpp-air-coremix | server] / =====> airmon_protocol ===> [gpp-air-console]->user perception | client***

    [-]
       airsh [air shell], though text-based, allows for targeted and complex
       multi- controller operation, such as addressing complex spans of
       channels, describing complex ramps for controllers and triggering
       gadgets such as player / recorder ([#] more to come in future). This
       functionality (conceptually) transcends simple
       physical-faders-and-knobs operating mode, although, of course, will
       always represent 'a different kind of game'. The combination of both,
       external physical controller and air shell might represent a win-win
       combination in controlling different cases and situations during live
       mixing.
    [-]
       gpp-air-midisender is actually a simple midi frontend talking to
       gpp-air-coremix sitting at server-side. It can be set up to control
       any parameters, basic or high resolution faders/knobs (nrpn).

    [-]
       gpp-air-console is bi-directionally connected to gpp-air-coremix and
       gpp-air-midisender slaves to gpp-air-console. All the crucial init
       parameters such as number of channels are automatically synchronized
       if changed on the server. Currently, the console intended as
       master-mixer monitoring device, but shall be developed [#] into
       client monitoring and organizing tool in order to provide complete
       mixing and input/output channels overview to each client (in the
       context of 'full' audio-scheme scenario as described above).

    .

PUREDATA gpp-air-console ELEMENT [client-side]
    [ gpp-air-console.pd <OSC.inaddress> <OSC.outaddress> ]

    [=] OSC receiver address and port (creation arg)
    [=] OSC sender (backlink) port (creation arg)
    [-] inlet1 and outlet1 for bi-directional communication with the
    optional gpp-air-midisender at the client side

PUREDATA gpp-midisender ELEMENT [client-side]
    [-] inlet1 : input for gpp-air-console commands [connected to console's
    outlet1]
    [-] inlet2 : midi setup - in
    [-] outlet1 : number of channels and input address/port monitoring state
    [-] outlet2 : gpp-air-console init-bang (querying server for crucial
    parameters such as number of channels and server-receive OSC addres
    [connected to console's inlet1]
    [-] outlet3 : midi setup - out

AIRMIX :: AIR CORE MIXER OSC COMMAND PROTOCOL

CHANNEL ADDRESSING
    The structure of the OSC message is:

    /airmix/<channel>/<controller> argument(s)

    where channel =

    master (in short: m)
    prelisten | preunmute (in short: p pu)

    <channel> | <channel_span> | <channel_selection_alias> - see
    chapter CHANNEL_SPAN AND CHANNEL_ALIASING

MONITORING
  <ch> mon / <ch> nom
    local per-channel monitoring; provides a pd gui window for each separate
    channel in the selected span (server-side).

  mix / xim
    show whole mixer-monitor in a single pd window. mixer-monitor is a gui
    element directly rendered by the server and is intended for direct
    monitoring on the server side.

  con / noc
    inform remote client (gpp-air-console user) to show or hide console gui
    window (a remote version of mixer-monitor in a single pd window)

CONTROLLERS
  master|m fader|f|level <airliner_vector>
    send airliner_vector to a master fader (both channels)

  master|m lfader|rfader|left|right <airliner_vector>
    send airliner_vector to a master fader (separate channels)

  <ch> fader|f <airliner_vector>
    send airliner_ector to a separate channel's faders

    * faders are dynamic. a ramp can be interrupted with a new ramp at any
    point and will continue to flow from that point on. Airliner vector
    curves will scale up/down to adapt to the height of the new window to
    cover.

  <ch> pan|p <airliner_vector>
    send an airliner_vector to a separate channel pan

    * NOTE master has no pan but both faders /stereo/ instead

AIRLINER_VECTOR
    is managed by gpp-airliner~.pm. Airliner can be bound to any mixer
    param, currently it controls faders and panning

    it will accept 1 - 4 input parameters:

    <value_to_reach [rms 0-1]> <time_of_operation [ms]>? <curve [string -
    see below]>? <initial delay [ms]>?

    where only the first parameter, <value_to_reach [rms 0-1]>, is
    compulsory. The other three, if omitted, will default to:

    <time_of_operation [ms]> defaults to 'jump' micro-fader time (50 ms)
    <curve [see]> defaults to 'lin' or 'linear'
    <initial delay [ms]> defaults to 0

    Currently available curves:

    jump micro-fader (50ms) linear curve
    lin linear
    sin sinusoidal (soft)
    hsin half-sinusoidal (equal power)
    log logarithmic, hard neck
    pow power (exponential), slow sudden attack

  <airliner_vector> examples
    0.9 => jump to 0.9
    0.422 7500 => slide to 0.422 in 7.5 seconds
    1 4230 sin => slide to 1 in 4.23 seconds following sinusoidal curve
    0.5 7600 pow 2000 => slide to .5 in 7.6 seconds following power curve,
    but start after 2 seconds from now

AUDIO PRODUCTION / PROCESSING TOOLS

  PLAY
    <ch> play <file*>

    Play a file (wav,aiff)

    <ch> play <file> <hh:mm:ss.uuu>

    Play a file from the selected timing on

    <ch> play <file> <hh:mm:ss.uuu> <hh:mm:ss.uuu>

    Play a file from the selected timing to the selected end

    <ch> play <file> <hh:mm:ss.uuu> <hh:mm:ss.uuu> +<hh:mm:ss.uuu>

    Play a file from the selected timing to the selected end with the
    selected +delay. Note that the player / looper delay parameter should be
    marked with +

    <file*> can be either a filename in connection with current working
    directory (see cd / dir directives) or an absolute path

    <ch> stop

    Stop current playing session at channel(s) <ch>

  LOOP
    <ch> loop <file>

    Loop whole file

    <ch> loop <file> <hh:mm:ss.uuu> <hh:mm:ss.uuu>

    Loop file clip from selected timing to selected timing

    <ch> loop <file> <hh:mm:ss.uuu> <hh:mm:ss.uuu> +<hh:mm:ss.uuu>

    Loop file clip from selected timing to selected timing with intermediate
    +delay

    <ch> stop

    Stop current looping session at channel(s) <ch>

  RECORD
    <ch> record <file>

    Record to file

    <ch> record <file> <hh:mm:ss.uuu>

    Record to file after initial +delay

    <ch> record <file> <hh:mm:ss.uuu> <hh:mm:ss.uuu>

    Record to file after initial lead-in a lenght long clip. The second
    figure being interval length. Timing display will change color to red
    when the recording actually starts.

    <ch> stop

    Stop current recording session at the addressed channel

  OTHER
    gpp-playhed will be added in future to enable complex manipulations of
    PLAY function (speed change, different ways of oscillating ramps,
    granulation/heartbeat etc...) [#] Performance-sensitive, will have to be
    tested in terms of mass channel addressing and potentially heavy
    monitoring OSC-traffic.

CHANNEL_SPAN AND CHANNEL_ALIASING
    <ch> refers to:

    channel number : send to a selected channel
    all : send to all channels
    even : send to even-numbered channels
    odd : send to odd-numbered channels
    selection span : send to a selection span which consist from '-'
    delimited ranges and ',' delimited lists, for instance 1,3,5-7

GLOBAL AND PER-CHANNEL COMMANDS

  solo, mute
    <ch> solo : set the channel 'solo' : set corresponding mutes and also
    send setsolo boolean signal
    <ch> unsolo | us : set the channel 'not solo' : set corresponding mutes
    and also send setsolo boolean signal
    master mute | m : mute master channel (monitored via setmute boolean )
    <ch> mute | m : mute selected channel (processed and monitored via
    setmute boolean )
    master unmute | u | um : mute the master channel (monitored via setmute
    boolean )
    master lunmute | lu : mute left master channel (monitored via setlmute
    boolean )
    master runmute | ru : mute right master channel (monitored via setrmute
    boolean )
    <ch> unmute | u : mute selected channel (monitored via setmute boolean )
    <ch> setmute <boolean> : set mute value (monitoring:
    /airmon/etc/<ch>/setmute <boolean>)
    master setlmute <boolean> : set l-master mute value (monitoring:
    /airmon/etc/master/setlmute <boolean>)
    master setrmute <boolean> : set r-master mute value (monitoring:
    /airmon/etc/master/setrmute <boolean>)
    mutelock directive is machine-generated and controls the second mute
    layer during solo operations
       NOTE: solo also operates on complex spans, for instance 1-3,7 will
       set solo the corresponding channels.

  solo and presolo switches policy
    solo and presolo switches do the following:

    solo or a group of solo commands (represented by a complex channel span
    will grab the mixer, disabling the rest of channels. If these are
    already muted, they will stay muted. If not, they will be solomuted (=
    mechanically locked to mute-state). If yes, they will remain muted, but
    an attempt to unmute them will put them into solomuted state.
    solo-ed channels can be muted/unmuted at will
    Any channel can be either added to or removed from the solo span.
    When the last solo channel is disabled, all solomuted channels will
    return to the previous state, either muted or unmuted.
    same policy applies on prelisten bus solo (presolo)

  prelisten bus
    ch prelisten | pl: add the channel to the pre-listening bus (separate
    prelisten monitoring audio port)
    ch premute | pm: remove the channel from the pre-listening bus (separate
    prelisten monitoring audio port)
    ch presolo | ps: set the channel as pre-listening solo : adjusts all
    premute values and also sends setpresolo boolean to the corresponding
    channel(s)
    ch unpresolo | ups: set the channel as pre-listening solo : adjusts all
    premute values and also sends setpresolo boolean to the corresponding
    channel(s)
    ch setpremute : boolean directive (fit for monitoring:
    /airmon/etc/<ch>/setpremute <boolean> )
    ch setsolopremute : machine generated solomute directive on presolo bus

  other globals
    human | nonhuman : set OSC input policy. nonhuman will: 1) not
    dereference complex spans (only per-channel or global addressing
    remains) and 2) treat all timing arguments as miliseconds (not
    hh:mm:ss.msc format). human reverts this behaviour to normal (enabled
    complex spans and hh:mm:ss.msc format)
    panic : all channel faders set to 0
    dir | cd : set global wavedata directory
    ls : get global wavedata directory
    trimfader : set trimfader time or trimfader type [#]
    centerpan : center all pans
    fullout : set all faders to full
    stereopan : set even-numbered faders to 0 and odd-numbered faders to 1
    (receiving in full stereo mode)
    globepan : evenly distribute panning across panorama 0-1 accross all
    channels
    lstracks : list numbers / configuration of input and output tracks
    through the rightmost outlet of [gpp-air-coremix] element (via set
    message)
    autosave : turn autosave (track names, mixer state, fader type) feature
    ON
    noautosave : turn autosave (track names, mixer state, fader type)
    feature OFF
    latency / latencystop : starts / stops measuring console latency (audio
    and control). The values are reported to the control (3rd) outlet of the
    [gpp-air-coremix] element (via set message)
    setmode : set server's monitoring mode (auto, mirror, coarse, off). See
    'Two main server-side monitoring modes' below.
    setff : set server's fanning factor (distance between serial OSC
    monitoring request, somewhere between 2 and 6, default 3 ) :: the serial
    monitoring requests (fader, pan) get distributed after the following
    formula:

       fader : (<ch> * <FF> * 2) msec DELAY
       pan : (<ch> * <FF>) msec DELAY

    alivesig start / stop : turn alive signals on / off. In the left bottom
    corner of the iConsole and CoreMixer there are rectangular symbols iCo
    and Srv. If alivesig is running they will show the state of connection:

       iCo is green : iConsole is connected (server-side monitoring)
       Srv is green : Server is connected (client-side monitoring)
       both red in case of opposite

    reset : erase autosave mixer data. By default, mixer has 2 sec interval
    autosave (autosave.txt). Persistence survives mixer-restart and
    mixer-resize. This command resets all parameters.
    fadertype lin / log : set linear or logarhytmic fader tipe. setfadertype
    boolean [ NOT YET IMPLEMENTED ON iCONSOLE!!! ]

INTERNAL CLIENT- COMMANDS
    These are client- (console) initiated

    /airmix/cinit/ bang => client signalizing server their own loadbang and
    querying for initial parameters such as number of channels, airdir etc.
    This request is handled separately on air-coremix input.

PRELISTEN BUS
    Unless in the light audio-scheme scenario Prelisten bus itself will not
    be provided by the server. It will be rendered by the client,
    gpp-air-console will render their own bus from all channels gathered via
    jacktrip.

    On the contrary, light mode [#] will provide prelisten bus, as well as
    master-mix.

    ch prelisten preunmute | pl pu: add the channel to the pre-listening bus
    (separate prelisten monitoring audio port) (monitoring:
    /airmon/etc/prelisten 1 )
    ch premute | pm: remove the channel from the pre-listening bus (separate
    prelisten monitoring audio port) (monitoring: /airmon/etc/prelisten 0 )
    ch presolo | ps: set the channel as pre-listening solo (monitoring:
    /airmon/etc/presolo )
    setprelevel : set the level of prelistening bus. Bound to 'jump' (50ms)
    ramp, not gpp-airliner. This know is per-ch only. There is no master
    volume. Available via /airmon/etc/[ch]/setprelevel

AIRMIX EXAMPLES [broadcast by the user/client sender such as airsh]

  MASTER
    /airmix/master/lfader 1 : set left master fader
    /airmix/master/rfader 0.235 : set right master fader
    /airmix/master/fader 0.5 : set both master faders

  CHANNELS
    /airmix/3/fader 1 : set fader #3
    /airmix/3-5,7/fader 1 : set faders #3,#4,#5 and #7
    /airmix/odd/fader 1 : set odd faders
    /airmix/all/fader 1 3000 sin : start all faders' ramp to 1, 3000 ms,
    sinusoidal curve
    /airmix/even/pan .5 6000 pow : start even pans' ramp to .5, 6 sec, power
    curve
    /airmix/4,5/pan 0 4000 log 6234 : start channel's 4 and 5 pan ramp to 0
    in 4 s, logarhytmic curve, after 6,234 sec delay
    /airmix/even/play test.wav : play file test.wav on even channels
    /airmix/even/play test.wav 0:05 : play file test.wav on the even
    channels from 0:05 to the end
    /airmix/even/play test.wav 0:05 : play file test.wav on the even
    channels from 0:05 to the end
    /airmix/1-4/loop test.wav 0:20 0:22.123 +0:03.120 : loop file test.wav
    on channels 1-4 clipped at 0:20 to 0:22.123 with 0:03.120 delay/gap
    /airmix/3/record myrecording.wav 0:25 : record to myrecording.wav after
    0:25 delay (with pre-count)

  CHANNEL- AND GLOBAL- ALIASES
    /airmix/odd mute : mute odd channels
    /airmix/3,4-5 solo : solo channels 3,4 and 5
    /airmix/panic : pan MASTERic (turn all faders down)
    /airmix/ls : get info about the server audio storage directory
    /airmix/trimfader : set trimfader time and type
    /airmix/centerpan : center all pans
    /airmix/stereopan : set all pans to stereo mode
    /airmix/globepan : equidistant placing of all pans
    /airmux/setmode : set server monitoring mode
    (...)

AIRMON :: AIR CORE MONITORING OSC COMMAND PROTOCOL

  MONITORING TACTICS
    Serves dispatching information about the mixer state to all subordinated
    (remote) web client subjects. While the data, dispatched on momentary
    basis, does not represent a problem regarding the OSC traffic demands,
    all continuous data types, such as fader pan etc, represent a challenge.
    Air engine will internally handle such types by the usage of
    signal-level streaming, therefore monitoring can be done using 3
    different tactics:

    A request : whole request (for instance: fader .5 3000 sin 6000) is
    transfered (copied from the airmix OSC input) to the web clients and
    clients themselves will take care about rendering itself, from begining
    to end. Not only gpp-airliner directive, but also timer requests can be
    given this way.
    B snapshot : current state of controller transferred on periodical basis
    (metronome pulse). Intermediate request data is sent using relatively
    low frequency in order to avoid OSC wire overheads
C contour : this tactics is actually a modification of snapshot tactics,
but will only send snapshot to the client(s) when RF (request_fulfilled)
signal on the respected controller is broadcast (this is called VR
(value_reached), also provided by gpp-airliner~). So instead of
metronome pulse, the initiative for broadcasting snapshot is based on
reaching controllers' border states. All intermediate request data is
ignored. This tactics alone can be used for low bandwidth cases, but
also to complement tactics A and B. With the A tactics, it can help
assure that the final state is obeyed regardless of potential
server/client desync. With the B tactics it can assure that the border
state information is delivered exactly in time, even if the server's
snapshot heartbeat is low.

  OSC CONTROLLER MAP

   MONITORING TACTICS:

    A. REQUEST
       /airmon/request/<ch>/<controller> <request params>

       any kind of user-request as such, copied directly from the OSC input
       for each respective controller, such as:

       /airmon/request/<ch>/fader <airliner~ params>
       /airmon/request/<ch>/pan <airliner~ params>

    A2. VIRTUAL REQUEST
       A request assembled by the server engine (not passed by the user) in
       order to encapsule bandwidth-demanding movement to be rendered by the
       client engine, such as:

       /airmon/request/<ch>/timer/<type> [start|stop] [initial_timing_ms]?
        display timer, where <type> can be "play" or "record"

    B. SNAPSHOT
       /airmon/snapshot/<ch>/<controller>

       controller state at the very moment

    C. CONTOUR
       /airmon/contour/<ch>/...

       separate reporting of basic border states :: the point of this
       tactics is to report some basic params that the client (web or pd)
       can use to render their own movement. There are several 'contour
       handlers', such as:

       ... rf/<controller> => controller rf when reached (request fulfilled
       => reached destination boolean (1=yes 0=not yet), fader or pan
       ... vr/<controller> => controller vr when rf reached (value reached
       => the actual destination value triggered when reached, fader or pan,
       and also play, record (border states)
       ... ac/<controller> => controller ac (active) : play, record and such
       things => player is active boolean (1=yes, 0=not)

    *note difference between rf and ac switches: rf policy is negative (=
    positive when not active) while ac policy is positive (= negative when
    not active).

   ALL THE REST
 In future, all data that cannot be ranged into the 3 main monitoring tactics, should be passed via /etc controller

    /airmon/etc/<anyparam> => other data or switches, non policy-classified
    /airmon/etc/<ch>/<anyparam> => other data or switches, non
    policy-classified : per-channel

    for instance:

    /airmon/etc/<ch>/filename/ => current file name distributed exactly
    before each play- or record- request
    /airmon/etc/<ch>/mute => mute boolean for the selected channel
    /airmon/etc/master/mute => master mute boolean (both channels)
    /airmon/etc/master/rmute => master mute boolean (right channel only)
    /airmon/etc/master/lmute => master mute boolean (left channel only)

   DIRECT SYS PARAMS
    System params (internal communication between air-coremix and console,
    without user interaction) are sent via /sys/ and /syscore/ controllers.
    /sys/ will deliver the messaga to the console frontend (shell that
    envelopes console-core) and /syscore/ will to the console core itself.
    These params is no thing the end user should be bothered with.

    /airmon/sys/CHNUM/ => number of channels, required by gpp-air-coremix
    creation argument - the console automatically resizes if the argument
    changes.
    /airmon/syscore/AIRDIR/ => airdir path storage (path itself stored as
    text)
    /airmon/syscore/SHOW/ [boolean] => show / hide console

TWO MAIN SERVER-SIDE MONITORING MODES BASED ON DIFFERENT MONITORING TACTICS

OFF :: monitoring disabled

    MIRROR and COARSE :: implementing contour and snapshot tactics:

       MIRROR : use both tactics => high bandwidth and low client capacity;
       will report border states and intermediate snapshots according to
       network capacity (tunable). Contour skeleton is used to prevent
       possible timing-based anomalies, especially with extremely lo
       frequency monitoring heartbeat.
       COARSE : use only contour tactic => low bandwidth and low client
       capacity; will only report border (crucial) states.

    AUTO :: use request and snapshot tactics => client themselves will
    render events; this is only safe when client is capable of running
    puredata console. Suitable for very low web bandwidth. Contour skeleton
    is used to prevent possible timing-based anomalies.
       Server can be set to either mode in terms of communicating with its
       console(s):

       /airmix/setmode mirror or airsh setmode mirror :: set mirroring mode
       (contour + snapshot)
       /airmix/setmode coarse or airsh setmode coarse :: set mirroring mode
       with only contour tactics enabled
       /airmix/setmode auto or airsh setmode auto :: set autonomous mode
       (all rendering based on request tactics data vectors)
       /airmix/lsmode :: list currently selected monitoring mode

AIR MIXER CONFIG FILES
    /var/air/data/mixer/airdir.txt - air current working directory
    /var/air/data/mixer/state/autosave.txt - mixer params state
    /var/air/data/mixer/state/autosave_chname.txt - fader type and channel
    names
    /var/air/data/airsh/airsh_log.txt - list of recently cast airsh commands

AIRSH EXAMPLES EXAMPLES> [broadcast by user/client]
    airsh m fader 1 2000 sin => fade complex curve

    airsh 1 fader .3 4000 log 2000 => fade after delay

    airsh play file.wav 0:12.345 0:15.012 +1:0.300 => play a clip after
    delay

    airsh loop file.wav 0:12.345 0:15.012 +1:0.300 => loop a clip after
    delay

    airsh rec 0:10 0:15 => record 15 seconds after 10 seconds delay

AIRMON PROTOCOL EXAMPLES [broadcast by gpp-air-coremix/server]
    /airmon/request/master/lfader/ 1 3000 sin

    /airmon/request/master/rfader/ 1 3000 sin

    /airmon/request/master/fader/ 1 3000 sin

    /airmon/snapshot/1/fader .346567

    /airmon/contour/master/rf/lfader 1

    /airmon/contour/master/rf/lfader 1

    /airmon/contour/3/ac/player 1

    /airmon/contour/1/timer/player start 3543 down

    /airmon/contour/1/timer/player stop

    /airmon/contour/3/timer/recorder start 0 up

AUTHOR
    Gregor Pirs <gregor.pirs@guest.arnes.si>

VERSION
    [3-1-2023]